## Slide 1
Better WASH for quality care in HEALTHCARE FACILITIES
Technical Module:
SANITATION
Insert date & location
WASH FIT

## Slide 2: Learning objectives
By the end of the session, participants should:
Be able to describe the minimum requirements for sanitation in health care facilities
Understand what “safely managed sanitation” is in the context of health care facilities
Understand how to make sanitation facilities user friendly, gender-inclusive and climate-smart
Know how to assess and work to improve the WASH FIT indicators for sanitation using an incremental approach

## Slide 3: Why is sanitation important?
Human faeces is the most common source of microbial pathogens (germs). One gram of human faeces has over 1,000,000,000 pathogens.
Safely-managed sanitation systems (i.e. toilets connected to a sewer and treatment plant or on-site treatment ) are a primary barrier that breaks the transmission within health facilities and to the surrounding community (also avoiding environmental pollution) by safely containing and treating excreta.
Aside from preventing infections, toilets that are clean and private are critical for patient wellbeing and dignity
Increasingly needed to help prevent the spread of antimicrobial resistance (AMR)
Notes: Suggested edits –

## Slide 4: Sanitation quiz
According to latest global estimates, what proportion of health care facilities do not have a toilet?
In a health care facility, toilets should be separated for _____ & _____ and for _____ & ______.
Toilets should have a hand washing station within _____ metres.
1 shower should be available for every _____ users.
Toilets should be cleaned every _________.
Notes: Spend 5 minutes discussing with the person next to you.

## Slide 5: Answers
Globally, 1 in 10 health care facilities do not have a toilet
In a facility, toilets should be separated for male & female and for patients & staff.
Toilets should have a hand washing station within 5 metres.
1 shower should be available for every 40 users.
Toilets should be cleaned every day.
Notes: Spend 5 minutes discussing with the person next to you.
1. Latest JMP data, published in 2020: 72% of health care facilities worldwide had access to improved and usable latrines in 2019. However, one in ten health care facilities globally, and three out of ten in sub-Saharan Africa, had no sanitation service in 2019.

## Slide 6: Brainstorm (Group work / breakout room)
1. Can you define a “safe sanitation system”?
2. In a health care facility, what are the other key considerations for safe sanitation?
© Linda Strande
Notes: Refer to Chapter 3 of Sanitation Guidelines for definitions: https://www.who.int/water_sanitation_health/publications/guidelines-on-sanitation-and-health/en/
Presenter to use flipchart and pens to get ideas from participants
Prompts
Consider all steps of the sanitation chain: Toilet, containment, conveyance, treatment, end use/ disposal. Note, there should be no reuse of HCF wastewater.
Sanitation measures to protect public health are both single- and multi-component, and include technologies.
Safe sanitation systems separate human excreta from human contact at all steps of the sanitation service chain carrying excreta from the toilet to its eventual safe use or disposal.
Health hazards associated with the sanitation chain may be microbial (the focus of the WHO guidelines), chemical or physical.

## Slide 7: A “safe sanitation system” is:
Designed and used to separate human excreta from human contact & groundwater
Separates excreta at all steps of the sanitation service chain – from:
  Toilet
  Containment – storage/treatment (onsite)
  Conveyance (including empty of containment)
  Treatment
  Disposal or end use
WHO (2018) Guidelines on Sanitation and Health (Refer to Chapter 3)
https://www.who.int/water_sanitation_health/publications/guidelines-on-sanitation-and-health/en/
Notes: Safe sanitation systems must meet these requirements in a manner consistent with human rights, while also addressing co-disposal of greywater, associated hygiene practices and essential services required for the functioning of technologies.
Prompts
Consider all steps of the sanitation chain: Toilet, containment, conveyance, treatment, end use/ disposal. Note, there should be no reuse of HCF wastewater.
Sanitation measures to protect public health are both single- and multi-component, and include technologies.
Safe sanitation systems separate human excreta from human contact at all steps of the sanitation service chain carrying excreta from the toilet to its eventual safe use or disposal.
Health hazards associated with the sanitation chain may be microbial (the focus of the WHO guidelines), chemical or physical.

## Slide 8: Sanitation options for health care facilities – on site treatment
Single, ventilated pit latrine
Source: Compendium of Sanitation Technologies. Eawag, Switzerland. 2018.
More information available at: https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-system-fact-sheets/en/
Pour flush or cistern toilets and bio-gas reactor or septic tank
Notes: Refer to Sanitation System fact sheets, Annex 1 of the WHO Sanitation Guidelines, also available at
https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-system-factsheets/en/

## Slide 9
11 system fact sheets covering:
Applicability
Design considerations
Operation and maintenance
Measures to protect public health
Accompanying sanitary inspection forms
Sanitation options for health care facilities
www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-guidelines/en/

## Slide 10: Sanitation options for health care facilities – on site treatment examples
Single, ventilated pit latrine
Source: Compendium of Sanitation Technologies. Eawag, Switzerland. 2018.
More information available at: https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-system-fact-sheets/en/
Pour flush or cistern toilets and bio-gas reactor or septic tank
Notes: Refer to Sanitation System fact sheets, Annex 1 of the WHO Sanitation Guidelines, also available at
https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-system-factsheets/en/

## Slide 11: Sanitation options for health care facilities – examples of off site transport or on-site treatment for larger volumes
Waste stabilization pond
Source: Compendium of Sanitation Technologies. Eawag, Switzerland. 2018.
Gravity sewer
Motorized collection
Anaerobic filter

## Slide 12: Performance of sanitation treatment options
Type | Pathogen reduction level | Treatment products and pathogen level | Best suited for/conditions required:
Containment technologies |  |  | 
Dry toilet with single pit | High (except Asacaris eggs) | Sludge stabilized into humus with low pathogens | Few users Medium soil permeability
Dry toilet with twin pits | High (except Asacaris eggs) | Sludge stabilized into humus with low pathogens | Few users Medium soil permeability
Flush toilet with open bottomed tank | Low | Liquid leachate high in pathogens is adsorbed aerobically into soil; removal dependent on soil conditions | Few users Water available Medium soil permeability
Flush toilet with septic tank connected to soak pit | Low | Liquid sludge has high pathogens, but these are absorbed aerobically in the soak pit | Average number of users Water available
Wastewater treatment technologies |  |  | 
Waste stabilization pond | High | Liquid sludge with low pathogens Effluent with low pathogens | Many users Water available Land available Personnel to maintain
Constructed wetlands | Medium | Plants-no pathogens Effluent with medium pathogens | Many users Water available Land available Personnel to maintain
Anaerobic upflow sludge blanket reactors | Low | Liquid sludge with high pathogens Biogas | Many users Water available Land available Personnel to maintain
Source: Adapted from WHO Guidelines on Sanitation and Health. 2018.

## Slide 13: Emptying and Conveyance – minimizing risk to waste handlers
Be aware of risks associated with handling wastewater and/or faecal sludge,
Equip workers to follow SOPs.
All workers to consistently & correctly wear PPE – gloves, masks, hats, full overalls and enclosed footwear – particularly where manual sewer work or emptying is required.

## Slide 14: Examples of climate impacts on sanitation
Climate change effect | Example impact on sanitation | Examples of associated health effects
More intense precipitation or inundation caused by sea-level rise | Flooding of on-site systems causing destruction of facilities, spillage, overflow and environmental contamination | Increased stress and potential exposure to violence and anxiety from lack of access to toilet facilities and reliance on open defecation Increased risks of water- and vector-borne diseases Increased exposure to faecal contamination
Long-term declines in rainfall and run‑off (leading to e.g. long-term drought etc.) | Declining water supply impeding function of water-reliant sanitation systems (e.g. flush toilets, sewerage); Increased demand for use of wastewater – especially in agriculture; shifting ground due to drying soils cracks or damages infrastructure | Increased risks of water- and vector-borne diseases (e.g. due to lack of water for flushing and cleaning resulting in poor sanitary conditions and poor hygiene, and changes in mosquito breeding) Increased open defecation and associated health risks Increase risk of water- and vector- borne diseases linked to untreated wastewater reuse
Higher temperatures (leading to e.g. warmer surface water and soil temperatures, heatwaves) | Malfunction, breakdown or inaccessibility of sanitation systems deterring safe sanitation behaviours (e.g. strong odours during heatwaves deterring use of latrines) | Health impacts resulting from unsafe use or non-use of sanitation systems (e.g. physical or mental health conditions)
Source: WHO, 2019. Discussion paper on sanitation, climate change and health. https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-and-climate-change20190813.pdf?ua=1

## Slide 15: Consider climate resilience of sanitation technologies
Source: WHO, 2019. Discussion paper on sanitation, climate change and health. https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-and-climate-change20190813.pdf?ua=1
Diagram of pit latrine
Resilience | Sanitation types
More resilient | Pit toilets Low flush on-site systems
Less resilient | High volume onsite systems Conventional sewerage Modified sewerage

## Slide 16: Quiz - Sanitation systems
Recall the example from the water section:
A primary care facility assists with 10 births a month.
Of these, on average, two women spend the night and the rest return home after a few hours.
In addition the staff treat, on average, 40 outpatients a week.
In addition there is a vaccination clinic a once a month that serves 100 children.
It is a rural facility and not connected to a sewer
What type of sanitation system would you recommend?
How many toilets?
© WaterAid
. https://www.who.int/water_sanitation_health/publications/ehs_hc/en/

## Slide 17: Answer
Facilities may not get a huge amount of use, apart from during vaccination clinics
Ventilated pit latrine or pour flush standing toilets and septic tank + leach field.
Once latrine is full cover and dig a new pit or having someone come empty the pit.
At a minimum: 3-4 toilets (1 or 2 for staff, 1 for male, 1 for female patients)
. https://www.who.int/water_sanitation_health/publications/ehs_hc/en/

## Slide 18: Climate resilient sanitation & wastewater management
Climate change impact | Example impact on sanitation | Examples of associated health effects
More intense precipitation (leading to extreme rainfall events, floods, landslides, etc.) | Flooding of on-site systems causing spillage, overflow and environmental contamination (e.g. in water supplies, floodwaters, surface water, soil). | Increased risks of water- and vectorborne diseases and antimicrobial resistance spread. Increased risks of health impacts associated with undernutrition.
Long-term declines in rainfall and runoff (leading to e.g. long-term drought, etc.) | Declining water supply impeding function of water-reliant sanitation systems (e.g. flush toilets, sewerage). | Increased risks of water- and vectorborne diseases (e.g. due to a lack of water for cleaning, resulting in poor sanitary conditions and poor hygiene). Increased risks associated with undernutrition resulting from interaction with diminished food production and intake in poor regions, and increases in diseases associated with undernutrition. Increased risk of water- and vector- borne diseases linked to untreated wastewater use for food production.
Higher temperatures (leading to e.g. warmer surface water and soil temperatures, heatwaves) | Malfunction, breakdown or inaccessibility of sanitation systems deterring safe sanitation behaviours (e.g. strong odours during heatwaves deterring use of latrines). | Health impacts resulting from unsafe use or non-use of sanitation systems (e.g. physical or mental conditions arising from suppressed urge to urinate/defecate).

## Slide 19: Sanitation & AMR: The role of health care facilities
Good manufacturing practices including wastewater treatment
Universal access to WASH (SDG 6.1 &6.2) in households to prevent avoidable use
Improve wastewater treatment for all sewage (SDG6.3)
Universal access to WASH in health facilities
Safe disposal of unused medicines

## Slide 20: What can be done?
Watsewater form HCF carries higher proportions of resistant bacteria and residues from last line of defense antimicrobials
Current evidence suggests that AMR-resistant bacteria is removed at the similar rates as other bacteria in sanitation treatment systems.
Safe collection, storage, and minimally secondary treatment of fecal waste (on or off site) should be prioritized to control spread of AMR. Higher level of treatment may provide additional protection.
For more on hygiene-related aspects of AMR, refer to the Hand Hygiene module

## Slide 21
Improving accessibility of sanitation services – meeting basic human rights
Accessing services can be challenging for
children
older people
pregnant women & women in labour
people with disability/disabilities
patients having had surgery & other medical procedures
women & girls due to social stigma and constraints
Common problems include:
squat toilets with no hand rails
insufficient space in toilets to move around
pathways to toilets (and water facilities) being difficult to use, particularly for people with limited mobility such as wheelchair users
Toilet adapted for children (lower and smaller seat)

## Slide 22: Managing and maintaining sanitation facilities
Toilets should be cleaned every day, and have a signed record of cleaning clearly visible.
Ensure a process is in place for rapidly addressing dirty or broken toilets, including through user feedback
Technical staff trained, and able to conduct regular operation and maintenance of plumbing, toilet and storage/treatment facilities.
© WaterAid, Tom Greenwood
Notes: Chapter 3: Operation and maintenance
• Cleanliness: the toilet and all surfaces of the room that it is in (e.g. bathroom, washroom, rest room, cubicle etc.) should be kept clean and free of excreta.
• Cleaning arrangements: Locally-available cleaning materials should be safely stored and used, and all people carrying out cleaning should observe safe working practices. Where the toilet is public or shared, a regular cleaning schedule should be in place, with provision made for supply of cleaning materials and personal protective equipment (PPE).
• Where dry toilets are used, a ready supply of ash, soil, lime or sawdust should be available within the facility, with which users can cover faeces after defecating. This helps to prevent flies and minimize
odours.

## Slide 23: Group activity
Look at the photos of WASH infrastructure and identify which are accessible/ inaccessible and why.
If you aren’t sure – what further information might you need to be able to help you decide?
Notes: Activity 2: Photos of Infrastructure
Split into small groups. Handout photos of WASH infrastructure to each group (or see following slide)
In groups, discuss whether the examples are accessible or not and why.
Participants may also wish to identify which Universal design principles have been addressed in the examples. What further information would you need to know whether it meets the universal design principles?
If there is time, have a brief feedback session where by you hold up each photo and discuss accessibility features.

## Slide 24: Global monitoring indicators
* ALL ARE APPLICABLE FOR COVID-19 *
Toilets/latrines should be onsite, usable (offers privacy, clean) and accessible.
Toilets are clearly separated for male and female or provide privacy (i.e. single stall/room) if gender neutral
At least one toilet should meet the needs of people with limited mobility and menstrual hygiene management needs.
Toilets should have a functioning hand hygiene station within 5m.
Notes: A toilet/latrine should have a door which is unlocked when not in use (or for which a key is available) and can be locked from the inside during use, there should be no major holes in the structure, the hole or pit should not be blocked, water should be available for flush/pour flush toilets, and there should be no cracks, or leaks in the toilet structure. It should be within the grounds of the facility and it should be clean as noted by absence of waste, visible dirt and excreta and insects).

## Slide 25: Global sanitation standards: Quantity continued
TOILETS
  Inpatients = 1 per 20 users
  Outpatients
    Minimum: 2 (1 for staff and 1 for patients),
    Ideally: 4 (male/ female staff & male/female patients; one should be handicap accessible)
SHOWERS
  Inpatients = 1 per 40 users
  Greywater
    Storm water should be drained through properly designed channels directing flow away from buildings and into a safe area in the environment.
Notes: Note: the minimum number of facilities is 2, this is to be realistic about what really small health care facilities can provide.

## Slide 26: Additional WASH FIT indicators – safely managed sanitation
Faecal sludge is fully contained for later emptying and treatment offsite or fully contained and treated in-situ.
Toilets are connected without leaks to a public sewer system. The sewer conveys excreta and wastewater with minimal leaks/overflows to treatment.
The treatment plant is designed to provide at least secondary treatment and performs to performance standards.
A stormwater (i.e. rainwater) and greywater drainage system is in place that diverts water away from the facility into a safe drainage or leachfield area
Greywater and/or stormwater is captured and reused for washing, cleaning, watering plants and toilet flushing

## Slide 27
Do these toilets meet global monitoring definitions and guidelines?
If not, how can they be improved?

## Slide 28: Sanitation in the context of COVID-19 Technical guidance takeaways
Hand hygiene: Frequent and effective hand hygiene - one of the most important prevention measures. Hand hygiene at the right time.
Water and sanitation: Existing WHO guidance on the safe management of drinking-water and sanitation services applies to the COVID-19 outbreak.
Co-benefits: Many will be realized through good WASH, including preventing millions of deaths each year caused by other infectious diseases.
WASH investments: Should be fundamental to all country preparedness and response plans.
Environmental hygiene: Effective inactivation on surfaces can be achieved within 1 minute using common disinfectants
1.
2.
3.
4.
5.
Guidance updated 23 April

## Slide 29: Survival of human coronaviruses in faces and wastewater
Media | Temp (OC) | Time | Removal | Reference
Dechlorinated tap water | 20 | 2 days | None surviving | Wang et al, J Virol Methods, 2005
Dechlorinated tap water | 23 | 8-12 days | 99.9% | Gundy et al Food Environ Virol, 2009
Hospital wastewater | 20 | 2 days | None surviving | Wang et al, J Virol Methods, 2005
Settled sewage | 25 | 14 days | 99.9% | Casanova, et al, Water Research, 2009
Wastewater | 23 | 2-4 days | 99.9 % | Gundy et al Food Environ Virol, 2009
Baby faeces | 20 | 3 hours* | None surviving | Lai, et al., Clinical Infectious Disease, 2005
Adult faeces | 20 | 1 day | None surviving | Lai, et al., Clinical Infectious Disease, 2005
Cotton gown | 20 | 5 min- 24 hours** | None surviving | Lai, et al., Clinical Infectious Disease, 2005
Various surfaces (review of 22 studies + one study on SARS-CoV-2) | Average 20 | 2 hours-9 days | None surviving | Kampf, et al., Journal of Hospital Infection, 2020; Dorelman, et al., NEJM, 2020
*Quicker die off attributed to lower pH in baby feces (pH 6-7).
**Quicker die off when there is a lower initial concentration of the virus.

## Slide 30: Safely managed sanitation in the context of COVID-19
WHO (2018) Guidelines on Sanitation and Health
https://www.who.int/water_sanitation_health/publications/guidelines-on-sanitation-and-health/en/
Safe management at every point of the sanitation chain; system should be able to meet an increase in demand
Important to check safety plumbing (e.g. sealed bathroom drains, backflow valves on bathroom sprayers and faucets)
Staff and patients should have separate toilets; where possible COVID-19 patients should have their own toilets
Regular cleaning and disinfection of bathrooms and anyone with risk of exposure to excreta should wear PPE
Practical, simple wastewater treatment technologies exist (e.g. septic tank + leach field; waste stabilization pond, burying and covering sludge)
Notes: Safe sanitation systems must meet these requirements in a manner consistent with human rights, while also addressing co-disposal of greywater, associated hygiene practices and essential services required for the functioning of technologies.

## Slide 31: Key takeaways
Sanitation facilities must be accessible to all users and protect against spread of infections and meet the wellbeing needs of patients
A toilet is not enough – fecal waste should be safely collected, transported, treated and disposed.
Regular cleaning and maintenance of toilet facilities is a low-cost, high impact measure to manage risks from fecal waste.
Spread of AMR can be controlled through safely managed sanitation systems – high-tech, high cost options are not necessary.
Existing WHO guidance on the safe management of drinking-water and sanitation services applies to the COVID-19 outbreak. NB: Staff and COVID-19 patients should have separate toilets to protect against spread of infection.

## Slide 32: Safely managed sanitation in the context of COVID-19
WHO (2018) Guidelines on Sanitation and Health
https://www.who.int/water_sanitation_health/publications/guidelines-on-sanitation-and-health/en/
Safe management at every point of the sanitation chain; system should be able to meet an increase in demand
Important to check safety plumbing (e.g. sealed bathroom drains, backflow valves on bathroom sprayers and faucets)
Staff and patients should have separate toilets; where possible COVID-19 patients should have their own toilets
Regular cleaning and disinfection of bathrooms and anyone with risk of exposure to excreta should wear PPE
Practical, simple wastewater treatment technologies exist (e.g. septic tank + leach field; waste stabilization pond, burying and covering sludge)
Notes: Safe sanitation systems must meet these requirements in a manner consistent with human rights, while also addressing co-disposal of greywater, associated hygiene practices and essential services required for the functioning of technologies.

## Slide 33: Questions?

## Slide 34: References
WHO (2008). Essential environmental health standards in health care. https://www.who.int/water_sanitation_health/publications/ehs_hc/en/
WHO (2018) Guidelines on Sanitation and Health https://www.who.int/water_sanitation_health/publications/guidelines-on-sanitation-and-health/en/
Compendium of Sanitation Systems and Technologies. 2nd Revised Edition https://www.eawag.ch/en/department/sandec/publications/compendium/
WHO (2015). Sanitation safety planning: manual for safe use and disposal of wastewater, greywater and excreta. http://www.who.int/water_sanitation_health/publications/ssp-manual/en/
WHO (2008). Essential environmental health standards in health care. http://www.who.int/water_sanitation_health/hygiene/settings/ehs_hc/en/
WHO (2011). Technical notes on drinking water, sanitation and hygiene in emergencies. Available at http://www.who.int/water_sanitation_health/publications/2011/tn9_how_much_water_en.pdf
WHO/UNICEF (2015). Water, sanitation and hygiene in healthcare facilities: Status in low-and middle-income countries and way forward. http://www.who.int/water_sanitation_health/publications/wash-health-care-facilities/en/
Swedish Red Cross (Ed.) (2008): Slide show of Swedish Red Cross water and sanitation module 4O ERU deployed in Philippines. Stockholm: Swedish Red Cross. URL: http://www.ifrc.org/Global/sw-watsan-eru-philippines0808.pdf [Accessed: 20.03.2015].
Peal, Andy; Evans, Barbara; Van der Voorden, Calolin (2010): Hygiene and Sanitation Software: An Overview of Approaches. Geneva: Water Supply & Sanitation Collaborative Council.