## Slide 1
Better WASH for quality care in HEALTHCARE FACILITIES
Technical Module:
HAND HYGIENE & WASH
WASH FIT Technical module
Climate Resilience

## Slide 2: Climate change – related definitions
Weather: atmospheric condition at any given time or place (measured in terms of temperature, precipitation…).
Climate: usually defined as the “average weather” over a period of time (usually 30 years).
Climate Hazard: event with potential to cause harm (e.g. drought, storm) or long-term change in climatic variables (e.g. temperature, precipitation).
Exposure: people, property or other elements in places or settings that could be adversely affected by hazards and that are thereby subject to potential losses.
Vulnerability: degree to which a system is susceptible to harm due to exposure to a perturbation or stress and the ability to cope, recover, or fundamentally adapt.
Risk: is the result of the interaction of physically defined hazards with the properties of the exposed systems (e.g. social vulnerability). Risk = (Hazard) x (Exposure) x (Vulnerability).
Notes: Weather: Atmospheric condition at any given time or place. It is measured in terms of such things as wind, temperature, humidity, atmospheric pressure, cloudiness, and precipitation. In most places, weather can change from hour-to-hour, day-to-day, and season-to-season.
Climate: in a narrow sense is usually defined as the "average weather", or more rigorously, as the statistical description in terms of the mean and variability of relevant quantities over a period of time ranging from months to thousands or millions of years. The classical period is 30 years, as defined by the World Meteorological Organization (WMO).
Climate hazard: is a physically defined climate event with the potential to cause harm (such as heavy rainfall, drought, storm) or long-term change in climatic variables such as temperature and precipitation (APF 2005). A hazard maybe a transient, recurrent event with an identifiable onset and termination such as a storm, flood or drought, or a more permanent change such as a trend or transition from one climatic state to another.
Exposure. The term exposure can be defined as “people, property, systems, or other elements in places or settings that could be adversely affected by hazards and that are thereby subject to potential losses”.
Vulnerability: The degree to which a system unit is susceptible to harm due to exposure to a perturbation or stress and the ability (or lack thereof) of the exposure unit to cope, recover, or fundamentally adapt (become a new system or become extinct) (Kasperson et al., 2000.) It can also be considered as the underlying exposure to damaging shocks, perturbations or stresses, rather than the probability or projected incidence of those shocks themselves (APF 2005).
Risk: is the result of the interaction of physically defined hazards with the properties of the exposed systems — i.e., their sensitivity or social vulnerability. Risk can also be considered as the combination of an event, its likelihood, and its consequences — i.e., risk equals the probability of climate hazard multiplied by a given system's vulnerability (APF 2005).

## Slide 3: Definition of Climate Change
CC refers to “a change in the state of the climate that can be identified (e.g. using statistical tests) by changes in the mean and/or the variability of its properties, and that persists for an extended period, typically decades or longer” (IPCC, 2007)
CC refers to “a change of climate that is attributed directly or indirectly to human activity that alters the composition of the global atmosphere and that is in addition to natural climate variability observed over comparable time periods” (UNFCCC)
Notes: Different definitions of climate change can be found among the literature. The most commonly referenced to date is that given by the IPCC Fourth Assessment Report (2007). The IPCC defines climate change as “a change in the state of the climate that can be identified (e.g. using statistical tests) by changes in the mean and/or the variability of its properties, and that persists for an extended period, typically decades or longer”.
It must be noted that the definition given by the IPCC refers to any change in climate over time, whether due to natural variability or as a result of human activity. This definition differs from that used by the United Nations Framework Convention on Climate Change (UNFCCC), where climate change refers to a change of climate that is attributed directly or indirectly to human activity that alters the composition of the global atmosphere and that is in addition to natural climate variability observed over comparable time periods.

## Slide 4
Social Infrastructure
Direct exposures:
Flood damage
Storm vulnerability
Heat stress
Indirect exposures: Mediated through natural systems: Allergens; Disease vectors, Increase water/air pollution
Economic and social disruption:
Food production/
distribution
Mental stress
Climate change
Precipitation
Heat
Flood
Storm
Drought
Increased water temperature
Health impacts
Undernutrition
Heart disease
Injuries
Vector-borne diseases
Infectious diseases
Social infrastructure
Direct exposures
Flood damage
Storm, drought vulnerability
Heat stress
Indirect exposures Mediated through natural systems:
Disease vectors
Water scarcity
Increased water/air pollution
Via economic and social disruption
Food production and distribution
Migration
Mental stress
Modified from Smith 2014
Pathways of climate change and human health
The health of human populations is sensitive to shifts in weather patterns and other aspects of climate change (IPCC)

## Slide 5
Environmental conditions
Baseline weather
Baseline air/ water quality
Geography
Soil/dust
Vegetation
Social Infrastructure
Direct exposures:
Flood damage
Storm vulnerability
Heat stress
Indirect exposures: Mediated through natural systems: Allergens; Disease vectors, Increase water/air pollution
Economic and social disruption:
Food production/
distribution
Mental stress
Climate change
Precipitation
Heat
Flood
Storm
Drought
Increased water temperature
Health impacts
Undernutrition
Heart disease
Injuries
Vector-borne diseases
Infectious diseases
Social infrastructure
Direct exposures
Flood damage
Storm, drought vulnerability
Heat stress
Indirect exposures Mediated through natural systems:
Disease vectors
Water scarcity
Increased water/air pollution
Via economic and social disruption
Food production and distribution
Migration
Mental stress
Modified from Smith 2014

## Slide 6
Environmental conditions
Baseline weather
Baseline air/ water quality
Geography
Soil/dust
Vegetation
Social Infrastructure
Direct exposures:
Flood damage
Storm vulnerability
Heat stress
Indirect exposures: Mediated through natural systems: Allergens; Disease vectors, Increase water/air pollution
Economic and social disruption:
Food production/
distribution
Mental stress
Public health capability and adaptation
Climate change
Precipitation
Heat
Flood
Storm
Drought
Increased water temperature
Health impacts
Undernutrition
Heart disease
Injuries
Vector-borne diseases
Infectious diseases
Social infrastructure
Direct exposures
Flood damage
Storm, drought vulnerability
Heat stress
Indirect exposures Mediated through natural systems:
Disease vectors
Water scarcity
Increased water/air contamination
Via economic and social disruption
Food production and distribution
Migration
Mental stress
Mediating factors
Socioeconomic status
Health and nutrition status
Primary health care
Early warning systems
Resilient health systems & HCF
Modified from Smith 2014
In summary
The most effective measures to reduce vulnerability in the near term are programs that implement and improve basic public health measures such as provision of clean water and sanitation, secure essential health care including vaccination and child health services, increase capacity for disaster preparedness and response, and alleviate poverty (IPCC)
WASH
WASH
WASH
WASH
WASH
WASH
WASH

## Slide 7
“all health care facilities and services are environmentally sustainable: using safely managed water and sanitation services and clean energy; sustainably managing their waste and procuring goods in a sustainable manner; are resilient to extreme weather events; and capable of protecting the health, safety and security of the health workforce”
WHO global strategy on health, environment and climate change (2019)
Goal for healthcare settings
https://www.who.int/phe/publications/global-strategy/en/

## Slide 8
Global environment
Climate change
Healthy
people
Climate-resilient and environmentally sustainable Health Care Facilities
Safely managed water and sanitation services
Clean energy and low-carbon health care
Sustainable waste management
Sustainable procurement
Resilient to extreme weather events
Protecting the health, safety and security of the health workforce
Sustainable infrastructure and technologies

## Slide 9: Approaches to Combat CC
ADAPTATION
MITIGATION
Adjustment in natural or human systems in response to actual or expected climatic stimuli or their effects, which moderates harm or exploits beneficial opportunities.
Examples:
Expanded rainwater harvesting
Water storage and conservation
Water reuse
Desalinization
Improved water efficiency
Technological change and substitution that reduce resource inputs and emissions per unit of output.
Examples:
Renewable energy supply (e.g. hydropower, solar energy)
Reforestation
Waste minimization
Composting of organic waste
Notes: There are two different approaches to combat climate change: adaptation and mitigation.
Mitigation: the IPCC defines mitigation as “Technological change and substitution that reduce resource inputs and emissions per unit of output”, and indicates that although several social, economic and technological policies would produce an emission reduction, with respect to climate change, mitigation means implementing policies to reduce GHG emissions and enhance sinks.
Adaptation: The Intergovernmental Panel on Climate Change (IPCC) defines adaptation in their 4th Assessment report (2007) as “adjustment in natural or human systems in response to actual or expected climatic stimuli or their effects, which moderates harm or exploits beneficial opportunities.” The IPCC further distinguishes between the types of adaptation as follows: anticipatory vs. reactive, private vs. public, and autonomous vs. planned.
According to the IPCC:
Anticipatory Adaptation—Adaptation that takes place before impacts of climate change are observed. Also referred to as proactive adaptation.
Reactive Adaptation—Adaptation that takes place after impacts of climate change have been observed.
Private Adaptation—Adaptation that is initiated and implemented by individuals, households or private companies. Private adaptation is usually in the actor's rational self-interest.
Public Adaptation—Adaptation that is initiated and implemented by governments at all levels. Public adaptation is usually directed at collective needs.
Autonomous Adaptation—Adaptation that does not constitute a conscious response to climatic stimuli but is triggered by ecological changes in natural systems and by market or welfare changes in human systems. Also referred to as spontaneous adaptation.
Planned Adaptation—Adaptation that is the result of a deliberate policy decision, based on an awareness that conditions have changed or are about to change and that action is required to return to, maintain, or achieve a desired state
With respect to UNICEF’s mandate to protect vulnerable children and considering our comparative advantage as an agency with strong links to community based action and government advocacy, UNICEF support for adaptive approaches will in the majority have the most effect.

## Slide 10
Addressing Climate change impacts requires higher up-front costs but is cost-efficient
Climate resilience objectives for healthcare facilities:
Health systems and WASH infrastructure designed to be climate resilient (risk informed)
Health systems built and operated to lower carbon emissions and foster environmental sustainability
Notes: Climate resilience objectives for health care facilities and systems are twofold. Firstly, health systems and the facilities and infrastructure within them need to be designed to become climate-resilient in response to climate hazards. Secondly, health care systems must be built and operated in a way that reduce their harmful impact on the environment and surrounding communities, lowering as much as possible greenhouse gases emissions.

## Slide 11: Global Frameworks
Notes: Climate Change is already having an impact on the access to, cost, quality and sustainability of WASH services for households, schools and healthcare facilities. Climate change can directly impact the quantity and quality of safe water resources, as well as the demand for that water.
Water-related climate risks arise from too much water, too little water, or polluted water. Climate change also affects the access to and functionality of sanitation facilities and services, and the practice of key hygiene behaviours.
The Strategic Framework for WASH Climate Resilience, was developed jointly by the Global Water Partnership (GWP) and UNICEF in 2014 and updated in 2017. The framework aims to provide the sector with a basic tool that is easy to follow and that can help bring coherence to existing but dispersed WASH climate resilient development programming. In agreement with the results framework that we will see in more detail in the next slides, some approaches that are tailored to health care facilities contexts.

## Slide 12
Framework for building climate resilient and environmentally sustainable health care facilities
Notes: The aim of this guidance is to enhance the capacity of health care facilities to protect and improve the health of their target communities in an unstable and changing climate; and to empower health care facilities to be environmentally sustainable, by optimizing the use of resources and minimizing the release of waste into the environment. Climate resilient and environmentally sustainable health care facilities contribute to high quality of care and accessibility of services, and by helping reduce facility costs also ensure better affordability. They are, therefore, an important component of universal health coverage (UHC).
The Figure illustrates the important dynamics affecting the climate resilience of health care facilities. Building on the concept of risk as a function of hazards, vulnerabilities and exposures, it depicts how hazards, in the form of a sudden event (a shock, such as a storm or sudden flood), or a slow-onset event (a stress, such as a drought, sea-level rise, or high volume of cases from a climate-related disease), will reduce the health care facility’s level of performance and capacity (left axis), through a combination of impacts on key facility elements (for example increasing exposures from WASH)

## Slide 13: CLIMATE RESILIENCE: WATER

## Slide 14: Consider climate resilience of water supply technologies
Source: WHO, 2009. Vision 2030: The resilience of water supply and sanitation in the face of climate change. https://www.who.int/water_sanitation_health/vision_2030_9789241598422.pdf?ua=1
Technology-based risk screening for WASH
Notes: Climate resilience needs to be embedded as part of WASH in HCFs, starting with the identification of climate risks in specific locations. Once the risks are understood, the water technologies (hardware) need to be climate resilient and to address specific climate risk identified.
In terms of water supply, springs, wells, rainwater harvesting from roofs are classified as least resilient. This is because of their vulnerability to contamination (especially during flood events or with rising groundwater levels), susceptibility to drought (limited storage) and/or the difficulty in preventing damage during floods. Springs and rainwater harvesting also offer little flexibility in terms of location. From an adaptation angle, climate change may also overwhelm the ability to deal with problems (e.g. flood damage) in situations where the quality and reliability of services is already poor.
There are water technological options available that are adapted for different climate risks. For example in a water scarce and drought prone area you might want to assess the use of taps with a presss function (so water only runs for a few seconds).

## Slide 15: Climate resilient water supplies – Reliability
Sufficient water storage at the HCF to buffer droughts periods
Alternative (back up) sources of water supply
Infrastructure needs to ready to withstand potential climate hazards (e.g. heavy rain, wind, floods, etc.)
Ensuring water availability at the HCF at all times and climate scenarios
Notes: Since water is an essential component of a HCF we need to make sure it will always be available, and this includes under all climate impacts and scenarios. Key considerations when dimensioning water supply for a new HCF, or when undertaking un upgrade of an existing one include:
Water storage at the HCF to buffer droughts periods (or failure of water supply system). It is necessary to design the water supply system with sufficient water storage capacity to have enough water during drought periods. This does not mean that a HCF should storage water for months but enough to be able to find a solution if, for example water supply relies on groundwater and aquifer levels drop during a drought period. In dry and hot areas, water storage should be covered to prevent water stored from evaporating. There are different technological options to allow for enough safe storing of drinking water.
Alternative (back up) sources of water supply need to be in place for the same reason as explained above. If the main source of water supply is groundwater, a back up system might be needed that could tap other sources of water, at least momentarily till a sustainable solution is in place. The principle of redundancy should always apply to water systems in a HCF (system to be dimensioned assessing scenario where main water source fails).
Climate resilient Water Safety Planning (WSP) helps addressing both points above. WHO has made available guidance for WSP in buildings, and further considerations on climate resilience are being finalized through an Addendum to the WASH FIT tool.

## Slide 16: Climate resilient water supplies – Low carbon
Long-term durability and low day-to-day running costs
Opportunity to reach higher levels of service and reliability
Reduced pressure on groundwater sources
Solar systems: affordable, sustainable and climate smart
Notes: Solar powered water systems are receiving growing attention as a means of scaling up affordable, sustainable and ‘climate smart’ services. To date, the majority of systems have been installed in rural communities, schools and health care facilities, replacing handpumps and motorized systems. Their key advantages, in addition to their zero emissions, include:
Long-term durability and low day-to-day running costs (unlike motorized systems); although the design and installation of systems can be technically demanding and higher up front costs (costs are decreasing however).
Solar powered water systems can offer HCFs not connected to a piped system the opportunity to step up the water ladder to reach higher levels of service, including increased reliability.
Reduced pressure on boreholes, and therefore less likelihood of failure, because solar powered systems typically pump and move water over an extended period of time. In addition, the tank storage included in system design can provide an important supply buffer (as mentioned in the previous slide). Taken together, these attributes may increase the overall resilience of the service in drying conditions or droughts.

## Slide 17: Climate resilient water supplies – efficiency, conservation and reuse
Behavior change: water conservation and efficiency in HCFs
Notes: Studies from the United States show how Health care facilities are the third-largest water consumers of all buildings in the country, and are responsible for 7 percent of water use among all commercial buildings. While this might not be exactly the same in the developing world, focusing on water conservation and efficiency in HCFs is becoming increasingly urgent due to the volume of water they require.
Reducing water use is a sustainable approach, specially in water scarce areas and those prone to droughts. It can also lead to major savings in terms of lower water and sewer bills. In addition, many water conservation techniques can be directly linked to reduced energy consumption, resulting in even greater cost savings. Examples in a HCF include low flow and self closing taps, low flow and dry urinals, sensitization of cleaners and users for example for handwashing, etc.
In some cases water can be reused for gardening.

## Slide 18: CLIMATE RESILIENCE: SANITATION

## Slide 19: Examples of climate impacts on sanitation
Climate change effect | Example impact on sanitation | Examples of associated health effects
More intense precipitation or inundation caused by sea-level rise | Flooding of on-site systems causing destruction of facilities, spillage, overflow and environmental contamination | Increased stress and potential exposure to violence and anxiety from lack of access to toilet facilities and reliance on open defecation Increased risks of water- and vector-borne diseases Increased exposure to faecal contamination
Long-term declines in rainfall and run‑off (leading to e.g. long-term drought etc.) | Declining water supply impeding function of water-reliant sanitation systems (e.g. flush toilets, sewerage); Increased demand for use of wastewater – especially in agriculture; shifting ground due to drying soils cracks or damages infrastructure | Increased risks of water- and vector-borne diseases (e.g. due to lack of water for flushing and cleaning resulting in poor sanitary conditions and poor hygiene, and changes in mosquito breeding) Increased open defecation and associated health risks Increase risk of water- and vector- borne diseases linked to untreated wastewater reuse
Higher temperatures (leading to e.g. warmer surface water and soil temperatures, heatwaves) | Malfunction, breakdown or inaccessibility of sanitation systems deterring safe sanitation behaviours (e.g. strong odours during heatwaves deterring use of latrines) | Health impacts resulting from unsafe use or non-use of sanitation systems (e.g. physical or mental health conditions)
Source: WHO, 2019. Discussion paper on sanitation, climate change and health. https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-and-climate-change20190813.pdf?ua=1

## Slide 20: Consider climate resilience of sanitation technologies
Source: WHO, 2019. Discussion paper on sanitation, climate change and health.
https://www.who.int/water_sanitation_health/sanitation-waste/sanitation/sanitation-and-climate-change20190813.pdf?ua=1
Resilience | Sanitation types
More resilient | Pit toilets Low flush on-site systems
Less resilient | High volume onsite systems Conventional sewerage Modified sewerage
Notes: For sanitation, resilience is directly linked to whether water is part of the technology process (e.g. sewerage), or indirectly where the capacity of the environment to absorb or reduce the effect of wastes is affected. The resilience of simple on-site sanitation is closely linked to climate scenarios. In drying environments, the risk of pollution may decline as the distance between the base of pits and groundwater (and hence travel time for pathogens) increases.
Nonetheless, on-site sanitation may still be vulnerable to damage from short-term flood events. Where rainfall and/or flooding increases, risks may be significant, especially if groundwater tables rise, with serious public health implications. In contrast, both declining water availability and increased flooding will pose major risks to sewerage and septic systems relying on water, although their potential adaptability is higher, at least with utility backstopping.
There are sanitation options available that are adapted for different climate risks. For example in a water scarce and drought prone area you might want to assess the use of dry urinals for men, etc.

## Slide 21: Adapting sanitation in HCFs to drought conditions
IMPROVED LATRINES AND SEPTIC TANKS |  |  | 
Adaptation option | benefits | Constrains | Additional comments
Investigate lower water use approaches for flushing and cleaning | Less water needed | Availability and cost of appropriate materials | Construction might need to change to account for slab type, plastic seals instead of water. If no water available then septic tanks are not a good option
Account for changes in soil moisture | Materials less likely to fracture reducing risk of groundwater contamination | Availability and cost of appropriate materials | Regular performance monitoring is needed looking for potential blockages and breaks
SEWERS |  |  | 
Adapt inspection and maintenance to detect blockages and include periodic flushing to avoid blockages | Prevents pipe damage and potential spills of untreated sewage | More operational expenditure | Need to monitor sewer performance for blockages and link to priority repair/rehabilitation
Technical changes to sewer design, layout and construction to cope with low/intermittent flows | Prevent blockages, damages, and spills with less water | Costs and technical feasibility | May include: more inspection chambers and rodding eyes, steeper falls; development of decentralize systems that can be managed independently; inception chambers to remove solids.
Adapt treatment processes to cope with low/intermittent flows | Can safe ward quality of receiving waters | Costs | Appropriate treatment processes might change (e.g. ponds or reed beds become viable in drying environments). Consider diluting flows before treatment.

## Slide 22: Adapting sanitation in HCFs to flooding conditions (I)
IMPROVED LATRINES AND SEPTIC TANKS |  |  | 
Adaptation option | benefits | Constrains | Additional comments
Siting of latrines in relation to flooding areas and water sources. | Minimize the risk of spread of fecal matter and water contamination | Siting options might be restricted within the HCF. | Sitting of latrines based on vertical and horizontal separation.
Adaptations to design and construction to prevent direct flood, damage, inundation and sand erosion | Minimize the risk of spread of fecal matter and water contamination | Availability of materials in local markets, local constructions skills and (potentially) cost | Options include: design to allow to regular emptying and post-flood rehabilitation to remove silt; installation of proper covers to prevent material flowing out; installing robust upper foundations; collar and footing to prevent against erosion; building of bunds to divert water flow away from latrine; planting of shrubs around pit to reduce erosion; switch to composting or dry latrines; non return valves on septic tanks.
Regular pumping or emptying of latrines to minimize sludge build-up | Prevents systems over-flowing. | Also need safe systems of transport, treatment and reuse/disposal | Implies a focus on the complete FSM chain with strong regulatory oversight, looking firstly at the market for and/or safe disposal of end products. Consider smaller pits to minimise quantity of faecal matter exposed to flooding.

## Slide 23: Adapting sanitation in HCFs to flooding conditions (II)
SEWERS |  |  | 
Adaptation option | benefits | Constrains | Additional comments
Strengthen flood defenses | Prevents inundation of sewerage system and treatment works | May not be sufficient to address risks associated with major floods, especially if HCF is in a low-lying area | Ideally as part of integrated flood defence and response strategy that extends beyond the HCF facility and involves different sector stakeholders
Preventative maintenance to clear drains and sewers regularly | Prevents overloading of infrastructure | May not be sufficient to address risks associated with major flood events. | Prioritise before the wet season. It might well need to be in a context beyond the HCF.
Adapt or design new systems – e.g. decentralised systems to minimise impact of local flooding; separate sewage and stormwater systems. | Protects infrastructure and treatment processes, and to minimises cross network risks |  | Decentralised systems can ‘diffuse’ the risk of network critical failures and enable more responsive HCF management. Cost can be reduced by using small-bore (simplified) designs located at shallower depths. Ideally, plan for separate sewage and stormwater removal, and gravity flow for sewers to reduce pumping costs and risk of failure.

## Slide 24: Low carbon sanitation in HCFs – contributing to mitigate climate change
Where viable and appropriate consider:
Using human waste as fertilizer and soil conditioner (e.g. composting latrines)
Generating biogas from human waste for energy
Using renewable energy sources for pumping wastewater

## Slide 25: CLIMATE RESILIENCE: HYGIENE

## Slide 26: Water Conservation, Efficiency and Reuse
In drought prone areas and those facing water scarcity water efficiency and conservation (e.g. push tabs), and water reuse (e.g. for gardening) need to be observed.

## Slide 27: CLIMATE RESILIENCE: HEALTH CARE WASTE

## Slide 28: Climate change impacts on healthcare waste management
Solid waste management can have exacerbating effects on the climate especially due to the emission of greenhouse gasses.
Changes in hydrology and temperature can affect the stability of waste containment structures
Increased rainfall and flooding can affect waste containers and lead to spreading of contaminants (including hazardous).
Even if facility is not flooded but the surroundings are, there can be disruption of the waste management chain (e.g. flooding of road, railway affect waste collection and off-site treatment).
Low lying coastal facilities are at increasing risk from inundation.
Notes: • Solid waste management can have exacerbating effects on the climate especially due to the emission of greenhouse gasses: Transporting health care waste in vehicles using fossil fuels, inadequate incineration, inappropriate incinerator technology, or the incineration of unsuitable materials results in GHG emissions and the release of pollutants into the air
• Changes in hydrology and temperature can affect the stability of waste containment structures (e.g. waste pits) within the health care facility
• Increased rainfall and flooding can lead to inundation of the facility and affect waste containers with spreading of contaminants (including hazardous). Consider this risk when planning and checking waste containers - placement and protection.
• Even if facility is not flooded but the surroundings are, there can be disruption of the waste management chain (e.g. flooding of road, railway affect waste collection and off-site treatment), so extra containment capacity needs to be in place at the facility.
• Low lying coastal facilities are at increasing risk from inundation.

## Slide 29: Adapting healthcare waste management to climate change
Sufficient containers and/or frequency of emptying planned and resourced in case demands on health care facilities increase
Pit/waste dump: In case of flooding, an alternative is in place including storing waste in elevated containers and/or transporting off-site
Waste pits are water tight to avoid flooding and are not over filled
Safe storage available for additional waste generated during climate-events and/or emergencies
Recovery Efforts after Dumpsite Collapse from Heavy Rains in Colombo, Sri Lanka

## Slide 30: Healthcare waste management contribution to mitigate climate change
Waste prevention and reduction: strategies are employed resulting in a reduction in the quantity of waste generated
Waste recycling: Non-hazardous waste is safely recycled
Phased out of incineration of medical waste: non-burn technologies are available to safely disinfect, neutralize or contain waste (e.g. autoclaves)
While incineration is phased out: Cardboard sharps/safety boxes are used in place of plastic boxes, to reduce harmful emissions when burned
Autoclave treatment of medial waste
Notes: Note: Autoclaves are closed chambers that apply heat and sometimes pressure and steam, over a period of time to sterilize medical equipment. Autoclaves have been used for a century to sterilize medical instruments for re-use.

## Slide 31: CLIMATE RESILIENCE: ENVIRONMENTAL CLEANING

## Slide 32: Clean water is a critical element of cleaning but might be scarce
Increase cleaning staff awareness of water conservation:
Avoid running the tap continuously for cleaning (specially outdoors spaces). Fill a bucket with the amount of water you need and use only the water inside to clean. This way you avoid opening and closing the tap every time you need to wet your cleaning cloth, which will also prevent a waste of water.
Check for a leaking tap. Cleaning the health facility is a great opportunity to check for anything in need of repair. When you turn on the tap to get water to clean, have a look at its function. If broken, report immediately as this can waste a great amount of water in a short period of time.

## Slide 33: Key takeaways
Climate change might seem a distant challenge to a health facility but it does impact essential services
WASH services need to be planned according to local and identified risks. What works in one location might not work in a different context.
Water storage, conservation and efficiency are a must in water scarce contexts and those suffering from increasing incidence of droughts.
Health care facilities exposed to floods need to carefully ensure that sanitation does not pose a risk to water supply and the environment